## Slide 1: Upflow Anaerobic Sludge Blanket (UASB)
Mary McGuinn

## Slide 2: AguaClara Cornell
Uphold and protect the fundamental human right to access safe drinking water.
Students lead the innovation process, learn from each other, and foster a collaborative environment.
Develop sustainable alternatives to current technologies.
Research. Invent. Design. Engage.

## Slide 3: UASB
z
Locally constructed, easily accessible materials
Operates without electric

## Slide 4: Pilot Study
Wastewater treatment plant in Ithaca, NY
3 Person home of waste water
Produces a maximum of 60 L/day biogas
(~ 20 minutes of cooking time)

## Slide 5: Advantages
Electric-free
Low space requirement
Biogas production (fuel, lighting)
Low sludge production
High efficiency
No mixing required

## Slide 6: Responsibilities
Sanitation for pathogens and nutrients
Chance of repairs
Collection and distribution of biogas

## Slide 7: Post-treatment Options
z

## Slide 8: Post-treatment
Important to improve the quality of water
  May be needed to reach quality standards
Eliminates more organic matter, nutrients, and pathogens than the UASB system can alone

## Slide 9
CONSTRUCTED WETLAND
+ Simple construction and maintenance, good for rural communities
- High land requirement, limited nutrient and pathogen removal
ACTIVATED SLUDGE
+ High efficiency: operational flexibility, BOD removal, nutrification
- High construction and operational costs
SEQUENCING-BATCH REACTOR
+ High efficiency and operational flexibility, nutrient removal
- Difficult start-up, need treatment and disposal of sludge

## Slide 10
DOWNFLOW-HANGING SPONGE
+ Low cost, easy maintenance, simultaneous nitrification/denitrification
- Low durability of packing material, further study needed
DISSOLVED-AIR FLOTATION
+ High loading rates, excellent removal of Crytosporidium and Giardia
- Need coagulant/flocculant, poor removal of ammonium and fecal coliforms
ROTATING-BIOLOGICAL CONTACTOR
+ No recirculation required, low maintenance, good E-coli removal
- High HRT required for low temperature, needs frequent maintenance

## Slide 11: Option: Trickling Filter
Flexible for our system
High efficiency
Low operational cost and land requirements
Cons: need packing media, need another method for ammonia removal and sludge treatment, and high construction costs

## Slide 12: Option: Stabilizing Pond
Simple and low maintenance
No energy requirement
High COD/BOD removal regardless of climate and SS production
Cons: requires land and high SS concentration

## Slide 13: Biogas
z

## Slide 14: About
Reliable and cheap energy feedstock
Healthier
Environmental impacts
Notes: Resp. issues arise with use of biomass (eg firewood)

## Slide 15: Advantages
Instant heat upon ignition (no pre-heating)
Burns cleanly
Releases less greenhouse gases
Slurry provides fertilizer
Heat can be controled

## Slide 16: Adaptations
Change appliances (cost)
Change cooking habits

## Slide 17: Use
Collect
Collect biogas from system in a durable inflatable container
Check
Check your appliance is biogas-friendly or modify a current appliance
Using current appliances results in low-performance
Use
Use with approved appliance
Cooking
Electricity
Refrigeration

## Slide 18: Biogas Compatible Devices Cooking
z
Gas Cooker/Stove Specific for Biogas
Simple and easy
Versatile in terms of pot type and size
Easy to clean and repair
Moderate cost
Modified Commercial Burner
This will result in low-performance
Expand the injector cross-section 2-4x
Increase size of jets (if needed)
Biogas pressure is between 75 to 150 mm of water column
Goal: achieve a stable, compact, bluish flame
Notes: Consumption rate: 150-400 L/hr for a biogas stove

## Slide 19: Modified Gas Stove
About
  Need to modify because butane/propane is approximately 3x more powerful to burn than biogas
  Experimental matter
  Preferred modified stove burner – Lotus
How to
  Expand injector cross section by 2-4x
  Increase size of jet openings (if possible)
  Can be done with electric drill
Lotus burner

## Slide 20: Other
z

## Slide 21: Collective System
Combine 2+ systems to provide for more people
Advantages:
Increased biogas production rate
Responsibilities are shared

## Slide 22: Savings Propane –> Biogas
25.70 lempira per liter
Propane: 1 liter/hr of cook time
Biogas: 150 liter/hr of cook time
1 day of biogas production from 1 UASB unit saves
~ 11.0 Lempira
1 year of biogas production from 1 UASB unit saves
~ 4015.0 Lempira
* Estimates from Tegucigalpa prices,
Notes: Update: Honduras gasoline prices, 04-Nov-2019 | GlobalPetrolPrices.com. (n.d.). Retrieved November 5, 2019, from https://www.globalpetrolprices.com/Honduras/gasoline_prices/
1 kg firewood ~= 200 L biogas https://akvopedia.org/wiki/Biogas_Combustion
20 lb tank ~= 20.5 hr cook time ~= 18 L
=> 17.8 L/20.5 hr cooking ~= 1 L/hr

## Slide 23: Biogas Results
Household Burner | Refrigerator (100 L) | Gas Lamp (60 W bulb)
60 L of biogas ⟹ 20 min of cooking time | 60 L of biogas ⟹ 120 min or 2 hr of cooling time (depends on outside temperature) | 60 L of biogas ⟹ 30 min of light

## Slide 24: Questions?
z

## Slide 25: References
(n.d.). Retrieved from http://alianzaporelagua.org/Compendio/tecnologias/t/t9.html.
Burning Blue Flames Gas Focus on Stock Photo (Shutterstock) 1499930861. (n.d.). Retrieved December 10, 2019, from https://www.shutterstock.com/image-photo/burning-blue-flames-gas-focus-on-1499930861
Biogas Appliances - energypedia.info. (n.d.). Retrieved November 5, 2019, from https://energypedia.info/wiki/Biogas_Appliances
Chong, S., Sen, T. K., Kayaalp, A., & Ang, H. M. (2012). The performance enhancements of upflow anaerobic sludge blanket (UASB) reactors for domestic sludge treatment – A State-of-the-art review. Water Research, 46(11), 3434–3470. https://doi.org/10.1016/J.WATRES.2012.03.066